## Slide 1
G-xxxx Night/IFR Operating Limitations
The aircraft is released from the limitation to operate by day and under Visual Flight Rules only, subject to the following additional alternative operational restrictions and requirements being complied with:
Limitations
The aircraft may be flown by day or night and under Visual Flight Rules or Instrument Flight Rules and in VMC or IMC.
Flight in known or forecast icing conditions is prohibited
Operation in IMC in areas of known or forecast thunderstorm activity is prohibited
Take off and landing in visibility less than 1500m is prohibited.
The aircraft may not be operated in IMC below 500ft agl, or 600 ft for a non-precision approach, or approach system limits, whichever is the greater.
Aft cg limit restricted to 75.3” aft of datum
Special Pilot Information
    A copy of the G-xxxx Pilot’s Operating Notes must be in the aircraft and available to the pilot.
    Alternator failure - in the event of an alternator failure, flight in IMC or at night must be terminated as soon as practicable but under no circumstances after more than 75 minutes, assuming load shedding is carried out immediately after the alternator fails. However due to the unknown initial state of charge it is recommended that additional margins of safety are used in deciding on choice of diversions.
    Lightning strike – the aircraft has not been certificated for lightning strike capability hence the limitation prohibiting flight in the vicinity of known or forecast thunderstorms.
    Pitot and static source. The aircraft is fitted with a heated pitot and separate static ports. An alternative static valve is fitted, located under the instrument panel which opens the static system to cockpit pressure. No position error calibration of the alternative static system has been carried out.
    Use of Flaps - when flying in IMC conditions, in order to reduce the pilot workload on the landing approach it is recommended that flaps are not lowered while in IMC conditions ie delay lowering flaps until after cloud break. Flight tests have shown that delaying the lowering of flap to 500ft agl does not cause an excessive workload.
    When making instrument approaches, in order to avoid a rough ride, it is recommended that airspeed is restricted to no more than Va (134 mph IAS)
    Night or IMC conditions must be left as soon as practical if a loss of GPS signal is experienced, due to a risk of the back-up AI presenting misleading attitude indication after about five minutes without a GPS signal.
Continued Airworthiness
The aircraft must be maintained in accordance with the Maintenance Schedule for LAA Administered Permit to Fly Aircraft as tailored for G-xxxx
Any maintenance other than permitted pilot maintenance must be certified by an LAA inspector with a night/IFR approval category
Minimum Equipment
All items of equipment listed in ‘Aircraft Equipment List G-xxxx’ must be fitted and serviceable if night/IFR flight is undertaken.
G-xxxx POH Issue 1 [Example] Jun 2022

## Slide 2
G-xxxx Operating Notes
Standard Speeds (Knots)
Climb
Climb: 90-115 (clean, faster is better),
Best glide speed: 90
Cruise
Basic S & L 2000 to 2500rpm 25 to 35 lit/hr
Leaned as far as possible below 65% power
Flying for endurance: 2100 rpm
Circuit
Take off – grass - half flap (nb flap limit speed), hard - no flap
Joining the circuit: - Take care to throttle back early to slow down
Downwind: clean 100 -120
Base: half flap 80
Approach: full flap 70
Instrument approach: clean 100 - 120
Threshold: 70
Flapless: +5 to base & approach speeds Short Field all above -5 (Power reqd on round out)
Max demonstrated cross wind: 15 knots (use full flap)
Forced Landing (without Power)
90 clean
G-xxxx Operating Notes
Pre flight features of Aircraft
Ensure tow bar is removed
Keep flaps full down to ease entry
Aircraft will tip on tail if 2 people stand on entry step, or wing, at same time
Fuel drains are 1 per wing
Remove pitot cover & air intake sponge
Pitot head may not heat up on the ground
Rudder cables will be slack on the ground
Fuel gauges on ground read approx 2 gals high
Min oil 3 marks down, max oil 2 marks down
Switch EFIS on, press ‘I Agree’ & align AHRS before engine start
After start
Switch on avionics,
  KLN-94 press ENT 4 times
  Txpdr – press STBY, check displayed alt (nb 1013mb), pwr cycle if no alt
  Adjust pilot & pass squelch as reqd
Use squelch (pull out vol knob) to assess radio volume settings.
Starting
Prime – 5 s – only operates with fuel pump on
During start, only pump throttle with engine turning (on starter or firing)
G-xxxx POH Issue 1 [Example] Jun 2022

## Slide 3
Handling Points
Protect nose leg & wheel at all times
Steer on ground using differential braking
Run up to 2000 rpm (min) for mag check max drop 175 max diff 150
Switch on & align autopilot while stationary before take-off
Ensure G meter is switched on
Pitch trim – clockwise nose down
Txpdr (usually) switches to ALT after take-off
Climb at full throttle, faster is better
Aircraft will accelerate quickly if nose is below the horizon with throttle > 15” MP
Stall is benign – relax back pressure to recover
Stall warning is “Angle, Angle, Push”
Autopilot not to be engaged below 1000’ AGL
Start to slow down before entering the circuit
Pay attention to speed on approach – little longitudinal stability with full flap
Flare well just prior to touchdown
Systems information
If GPS signal is lost attitude provided by standby attitude indicator (GRT Mini-B) will fail within 5 minutes. Return to VMC as soon as practicable
G-xxxx Operating Notes
G-xxxx Operating Notes
Systems information
Emergency alternate static – pull peg behind throttle
Avionics special features
  EFIS – press left most button to cancel warning light
  D on audio panel will mute EFIS audio warnings
  EFIS – press left most button (RETURN) to exit menus
  EFIS – press left most button (PAGE) to change display
  EFIS – press either knob to see knob list, rotate to select
  COM2 – pres COM to tune Com radio, press NAV to tune Nav radio
Load shedding in event Alternator failure
  Turn on ‘Endurance Bus’ switch
  Switch off Master switch
  Battery capacity for normal loads
    Night 75 minutes
    Day 75 minutes
    EFIS internal battery 60 minutes
  Return to VMC as soon as practicable Night – land as soon as practicable
Shutdown information
Turn off radios (leave intercom on)
Run engine at 1000rpm for 30 secs before shutdown
Leave G meter keep alive on
Download EFIS flight file, if required, before switching master off
EFIS will remain on for 30 seconds after master switch is turned off.
G-xxxx POH Issue 1 [Example] Jun 2022

## Slide 4
G-xxxx Operating Notes
Aerobatics
Max aeros weight = 1375lb
Empty weight = 1056lb
Full fuel = 228lb
200lb pilot, max aeros fuel = 10 gals per side
Intentional spinning prohibited
Standard spin recovery is effective
Speeds in Knots
Va 117
Flick Roll avoid
Aileron roll 100 - 160
Barrel roll 120 - 160
Stall turn 120 – 160 Caution – engine stops in vertical resulting in low rudder power for turn; risk of a tail slide
Loop 130 - 160
Loop and roll off top 130 – 160
The LAA says: Warning: this is a high performance aircraft in which care is required particularly during aerobatic manoeuvres to avoid exceeding structural limits and/or maximum permitted airspeeds. In the event of an inadvertent erect spin the aircraft responds to standard recovery actions ie throttle closed, check ailerons centred, apply full opposite rudder followed by progressive forward stick until rotation ceases.
Aerobatics prohibited with baggage in baggage compartment.
G-xxxx Operating Notes
Airworthiness Speeds
ASI has colour markings iaw international practice
Beware low flap limiting speed, especially on go-around
With Sensenich metal propeller engine is limited to 2600rpm
Loading
Max aft cg for IMC flight is 75.3” aft of datum
CG moves backwards as fuel is burned
For 2 x 180lb pilots max baggage is 58lb to remain inside 75.3” limit with 6 US gals of fuel
G-xxxx POH Issue 1 [Example] Jun 2022